EXPLODED VIEW

MILANO

EXPLODED VIEW

GENERAL SPLITTING UP

- UPPER PART

- COMPLETE SIDE WALL

- BOTTOM PART

- UPPER PART

1.1 INTERNAL FINISH

1.2 SHELF

1.3 BOTTOM PLANE

1.4 FRAME 4 DOORS

1.5 CONTROL PANEL – TOP

1.6 ELECTRICAL BOARD – TOP

1.1 INTERNAL FINISH

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIJ002 | TOP COVER 1208 | GALVANIZED SHEET SKIMPAS 7/10 | 6M-250070403 | 6M-187070403 |
| 2 | MIJ003 | TOP SUPPORT OMEGA |  | 6M-187040026 |
| 3 | MIG003 | LATERAL BACK PANEL 922 PAINTED | GALVANIZED SHEET SKIMPAS 7/10 | 2M-187040059 |
| 4 | MIG011 | CEILING AIR DIVERTER SUPPORT BRACKET | GALVANIZED SHEET 10/10 | 6M-187040024 |
| 5 | MIG009 | UPPER CEILING AIR DIVERTER SHEET 2 PAINTED | GALVANIZED SHEET 10/10 | 2M-250040023 | 2M-375040023 |
| 6 | MIG008 | UPPER CEILING AIR DIVERTER SHEET 1 PAINTED | GALVANIZED SHEET 10/10 | 2M-250040022 | 2M-375040022 |
| 7 |  | EVAPORATOR ASSEMBLY H225 SC.V.R22 S. |  | 2M-250280002 | 2M-375280002 |
| 8 | MIR001 | LATERAL RACK PAINTED H225 |  | 2M-187040053 (SX) |
|  |  |  |  | 2M-187040052 (DX) |
| 9 | MIF005 | AIR CLOSURE FIXING | GALVANIZED SHEET SKIMPAS 7/10 | 6M-187040020 (SX) |
|  |  |  |  | 6M-187040019 (DX) |
| 10 | MIA016 | OMEGA BACK PLATE SUPPORT |  | 6M-187040007 |
| 11 | MIA010 | FRONT PLATE SUPPORT BRACKET PAINTED |  | 2M-187040006 |
| 12 | MIG002 | CENTRAL BACK PANEL 922 PAINTED |  | 2M-187040060 |
| 13 | MIJ005 | FRONT FINISH NIGHT COVER SUPPORT PAINTED | GALVANIZED SHEET 10/10 | 2M-250070006 | 2M-375070006 |
| 14 | MIA011 | DISPLAY CASE FRONTAL SUPPORT 1200 | GALVANIZED SHEET 20/10 | 6M-250060001 |
| 15 |  | FANS HOLDER |  |  |  |
| 16 | MIG001 | SUCTION GRID PAINTED 2496 | GALVANIZED SHEET 10/10 | 2M-250040008 | 2M-375040008 |
| 17 | MIG007 | CONVEYOR PLATE SUPPORT BACK PANEL PAINTED | GALVANIZED SHEET 10/10 | 2M-250040025 | 2M-375040025 |
| 18 | MIJ001_TOPN | NEW TOP PROFILE PAINTED | SILVER PLATED CONVEYOR PROFILE 0L 001-1 L.6100 | 2M-250070402 | 2M-375070402 |
| 19 |  | DIGITAL THERMOMETER CC10030000-A |  | 4131307 |
| 20 | MIC001 | PANEL FOR CONTROL MASK PAINTED | GALVANIZED SHEET 10/10 | 2M-250020033 | 2M-375020033 |
| 21 |  | BLACK BIPOLAR SWITCH R515KKFTOFA BOARD |  | 4113524 |

1.1.1  CENTRAL RACK

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIG006 | CENTRAL RACK BRACKET | GALVANIZED SHEET 15/10 | 6M-187040005 |
| 2 | MIA008-225 | CENTRAL RACK PAINTED H225 |  | 2M-187040054 |

1.1.2 FANS HOLDER

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIF002 | FANS HOLDER | GALVANIZED SHEET SKIMPAS 7/10 | 6M-250040015 | 6M-375040015 |
| 2 | MIF 004 | FANS AIR CLOSURE | GALVANIZED SHEET SKIMPAS 7/10 | 6M-187040018 (SX) |
|  |  |  |  | 6M-187040017 (DX) |
| 3 | MIF008 | FANS HOLDER CASE | GALVANIZED SHEET SKIMPAS 7/10 | 6M-250040016 | 6M-375040016 |
| 4 |  | MOTORFAN "PP" 4715 MS23TB10 A00 |  | 4241007 |

1.1.3 EVAPORATOR

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIF006-1 | EVAPORATOR MILANO |  | 4220153 | 4220154 |
| 2 | MIF001 | EVAPORATOR COVER | GALVANIZED SHEET SKIMPAS 7/10 | 6M-250040011 | 6M-375040011 |
| 3 |  | VALVE THERMOSTAT.R404 TES 2 CART. |  | 4251313 |
| 4 |  | EXTERNAL EQUALIZATION TUBE |  | 2M-250280004 | 2M-375280004 |
| 5 |  | VALVE BULB |  |  |
| 6 |  | SUCTION LINE |  |  |
| 7 |  | SUCTION TUBE |  |  |
| 8 |  | DISTRIBUTOR |  |  |
| 9 | ISC013 | EVAPORATOR AND AIR CHANNEL STAINLESS STEEL RESISTANCE 812 W |  | 4120152 | 4120153 |
| 10 | MIF003 | LOWER EVAPORATOR COVER | GALVANIZED SHEET 10/10 | 6M-250040012 | 6M-375040012 |
| 11 | ISC013 | EVAPORATOR AND AIR CHANNEL STAINLESS STEEL RESISTANCE 812 W |  | 4120152 | 4120153 |

1.2 SHELF

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIK001 | THREAD SHELF MILANO |  | 4333256 |
| 2 | MIK002 | RIGHT CONSOLE FOR MILANO SHELF PAINTED | RIGHT SHELF 400 GALVANIZED | 2M-1870A0006 |
| 3 | MIK002 | LEFT CONSOLE FOR MILANO SHELF PAINTED | LEFT SHELF 400 GALVANIZED | 2M-1870A0007 |
| 4 | MIK005 | PRICE HOLDER PROFILE | PVC PROFILE COEXTRUDED 3800MM 1D-001 | 2M-1870A0008 |

1.3 BOTTOM PLANE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIK004 | BOTTOM PLATE WITHOUT HOLE, PAINTED | GALVANIZED SHEET 10/10 | 2M-1870A0003 |
|  |  | BOTTOM PLATE WITH HOLE, PAINTED |  | 2M-1870A0004 |
| 2 | MIK008 | PRICE HOLDER SUPPORT STOP, PAINTED | GALVANIZED SHEET 10/10 | 2M-1870A0010 |
| 3 | MIK007 | GREY BOTTOM PRICE HOLDER SUPPORT | GALVANIZED SHEET SKIMPAS 7/10 | 6M-1870A0009 |
| 4 | MIK009 | PRICE HOLDER PROFILE BOTTOM PLATE | PVC PROFILE COEXTRUDED 3800MM 1D-001 | 2M-1870A0011 |

1.4 FRAME 4 DOORS

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | FRAME 4 DOORS MILANO C6/2 2498X1066 RIGHT |  | 4337484 | 4337486 |
|  |  | FRAME 6 DOORS MILANO C6/2 3749X1066 RIGHT |  |  |  |
| 2 |  | DOOR 3VR M/AL.N.E15789 604X1028 RIGHT |  | 4337487 |

1.5 CONTROL PANEL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIC004 | TOP BALLAST COVER AND DISPLAY CASE |  | 6M-187020036 |
| 2 |  | PVC WIREWAY 40 X 40 |  | 4110408 |
| 3 | MIC003 | TOP BALLAST HOLDER AND DISPLAY CASE |  | 6M-187020035 |
| 4 |  | BALLAST 30 W |  | 4115103 |
| 5 |  | TERMINAL BOARD |  |  |  |

1.6 ELECTRICAL BOARD

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | TO BT-057 | ISOLATOR PLATE |  | 6T-156020026 |
| 2 | MIC006 | TERMINAL BOARD PLATE COVER |  | 6M-187020037 |
| 3 |  | FILTER |  |  |
| 4 | TO BT-110 | PLOUGHING UP COVER PLATE FOR CONNECTOR |  | 6T-156020027 |
| 5 |  | TRANSFORMER |  |  |
| 6 |  | THERMOSTAT |  |  |
| 7 | MIC007 | TERMINAL BOARD PLATE | IRON SHEET GALVANIZED 15/10 |  |
| 8 |  | PVC WIREWAY 40 X 40 |  | 4110408 |

2. COMPLETE SIDE WALL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | MIM010_TOPN | SIDE WALL EXTERNAL FINISH H225 | GREY PLAST. N1 8/10 | 6M-187080657 (SX) |
|  |  |  |  | 6M-187080607 (DX) |
| 2 | MIM003 | CURVED BASE GLASS 4T/9/4/9/4T |  | 4190283 |
| 3 | ISD004-CP | GLASS VERTICAL PVC PROFILE CA. | GLASS CHAMBER VERTICAL PROFILE CAPRI / SIC. L.3000 MM | 2C-187080012 (SX) |
|  |  |  |  | 2C-187080011 (DX) |
| 4 |  | HEAD SIDE WALL SARDEGNA SKIMMED |  | 2S-18708T052 (SX) |
|  |  |  |  | 2S-18708T002 (DX) |
| 5 | MIM004_TOPN | VERTICAL SIDE WALL FINISH MILANO |  | 2M-187080453 (SX) |
|  |  |  |  | 2M-187080403 (DX) |
| 6 | ISM018_TOPN | LATERAL TROLLEY STOPPER PROFILE | TROLLEY STOPPER PVC PROFILE SM VE. NEW L. 4500 1E-021 | 2M-187080405 |
| 7 | ISM023-CP | LATERAL MINIGONNA PROFILE | BLACK MINIGONNA PROFILE ATLANTA L. 2500 | 2C-187080010 |
| 8 | MIM018 | LATERAL MINIGONNA SUPPORT | PLAST. N12SM 8/10 | 6C-187080409 |
| 9 | MIM020 | SIDE WALL LATERAL BASE | PLAST. N12SM 8/10 | 6C-187080408 |
| 10 | ISM012 | LATERAL BASE BRACKET |  | 6C-187080007 (SX) |
|  |  |  |  | 6C-187080006 (DX) |
| 11 | 1B-129 | GREY TROLLEY STOPPER NY R59 |  | 4351705 |
| 12 | MIM001 | TROLLEY STOPPER SUPPORT ALUMINIUM PROFILE | SILVER-PLATED GLASS CHAMBER SUPPORT PROFILE ISM017-CP | 2M-187080054 (SX) |
|  |  |  |  | 2M-187080004 (DX) |
| 13 | ISM022-CP | ANGULAR VER. R58 SP. CAPRI 7042 | UNFINISHED ANGULAR R58 | 2C-187080021 |
| 14 | ISM020-R007 | RAIL-HAND ANGULAR |  | 4100337 |
| 15 | ISD001 | GLASS SUPPORT LATERAL CLOSURE CA. |  | 6C-187040032 |
| 16 | MIM002 | GLASS CHAMBER RAIL-HAND PROFILE | SILVER-PLATED GLASS CHAMBER RAIL-HAND PROFILE ISM021-CP | 2M-187080002 |
| 17 | TOM003 | VERTICAL TOP HEAD TOP MI-TO | GALVANIZED SHEET 15/10 | 2M-187080408 |

3. BOTTOM PART

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | LAMPS HOLDER |  |  |  |
| 2 |  | INSET |  |  |  |
| 3 |  | AIR OUTLET MASK 1250 |  | 2C-250042043 |
| 4 |  | INTERNAL FINISH |  |  |  |
| 5 |  | FRAME |  |  |  |
| 6 |  | SLIDE |  |  |  |
| 7 |  | DRAIN MILANO |  | 2M-250050000 | 2M-375050000 |
| 8 |  | CONTROL BOARD |  |  |  |
| 9 |  | FRONT GLASS |  |  |  |
| 10 |  | CONTROL BOARD |  |  |  |
| 11 |  | DISPLAY AREA CP P110 |  | 2C-2500A0000 | 2C-3750A0000 |

3.1 LAMPS HOLDER

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | BALLAST 36 - 40 W |  | 4115104 |
| 2 | MIC005 | LAMPS HOLDER AND UNDER BODY RESISTANCE | GALVANIZED SHEET SKIMPAS 7/10 | 2M-250020034 | 2M-375020034 |
| 3 |  | LAMPS HOLDER 249 TS "UL" |  | 4114727 |
| 4 |  | NEON F 36 T8 CW WHITE D.26 L 1200 |  | 4114304 |
| 5 |  | UNIVERSAL STARTER FS 11 |  | 4116001 |
| 6 |  | LAMPS HOLDER + STARTER HOLDER 249 TCR "UL" |  | 4114726 |

3.2 INSET

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | BACK SKIMMED RISE INSET |  | 2C-250000008 | 2C-375000008 |
| 2 | SAG011 | INSET RESISTANCE COVER | STAINLESS STEEL 304 SB+PRO 8/10 | 6S-250040014 | 6S-375040014 |

3.3 AIR OUTLET MASK

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | SAG008 | AIR OUTLET SPACER PAINTED | GALVANIZED SHEET 10/10 | 2S-187040012 |
| 2 | SAG009-1250-L4 | SHEET 004 AIR OUTLET 2500 PAINTED |  | 2S-250040011 |
| 3 | SAG009-1250-L3 | SHEET 003 AIR OUTLET 2500 PAINTED |  | 2S-250040010 |
| 4 | SAG009-1250-L2 | SHEET 002 AIR OUTLET 2500 PAINTED |  | 2S-250040009 |
| 5 | ISG009-1250-L1 | FOIL 1 PAINTED | GALVANIZED SHEET 10/10 | 2C-250041044 |

3.4 INTERNAL FINISH

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | ISG010 | GLASS CHAMBER SUPPORT BRACKET PAINTED |  | 2C-187040009 (SX) |
|  |  |  |  | 2C-187040007 (DX) |
| 2 | ISG016 | FRONT MASK PAINTED | GALVANIZED SHEET 10/10 | 2C-250040015 | 2C-375040015 |
| 3 | SAG018 | HARDENED BAFFLE GLASS SA-CP-MI 2493X273 |  | 4192027 | 4192030 |
| 4 | ISG005 | LATERAL BACK BRACKET PAINTED | GALVANIZED SHEET 25/10 | 2C-187040038 (SX) |
|  |  |  |  | 2C-187040037 (DX) |
| 5 | ISG004 | BACK MASK PAINTED | GALVANIZED SHEET 10/10 | 2C-250040013 | 2C-375040013 |
| 6 | ISG003 | CENTRAL BACK BRACKET PAINTED |  | 2C-187040005 |
| 7 | ISG020-CP | FRONT BAFFLE GLASS SUPPORT PROFILE | LIBANO PROFILE 4500MM | 2C-250040036 | 2C-187040036 |
| 8 |  | REFRIGERATION SC. V. R22 S. P110 |  | 2C-250180000 | 2C-375180000 |
| 9 |  | FANS HOLDER |  |  |  |
| 10 | ISG028 | HEAD STOPPER SARDEGNA |  | 6S-18704T002 (SX) |
|  |  |  |  | 6S-18704T001 (DX) |
| 11 | 1A-014 | PROTECTION SUBSTOPPER ST60 | PLAST. | 4333113 |
| 12 | ISB003 | FRONT BASE BRACKET | IRON SHEET GALVANIZED 15/10 | 6C-187070010 |
| 13 | ISB008 | FRONT MINIGONNA PROFILE | BLACK MINIGONNA PROFILE ATLANTA | 2C-250070012 | 2C-375070012 |
| 14 | ISJ002 | FRONT SUPPORT BRACKET |  | 6C-187070005 |
| 15 | 1E-004 | FRONT BASE FINISH F350 | PLAST. N12SM 8/10 | 6V-250070007 | 6V-375070007 |
| 16 | 1E-002 | FRONT BASE F350 | PLAST. N12SM 8/10 | 6V-250070009 | 6V-375070009 |
| 17 | ISJ001 - CF | FRONT PANEL WITH HOLE PAINTED | GALVANIZED SHEET SKIMPAS 7/10 | 2C-250070002 |
|  | ISJ001 - SF | FRONT PANEL WITHOUT HOLE PAINTED |  | 2C-250070004 |
| 18 |  | DIGITAL THERMOMETER CC10030000-A |  | 4131307 |

3.4.1 EVAPORATOR

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | ISF001 | EVAPORATOR COVER P110 | GALVANIZED SHEET SKIMPAS 7/10 | 6C-250040016 | 6C-375040016 |
| 2 | ISC014 | DRIP AND EVAPORATOR STAINLESS STEEL RESISTOR |  | 4120951 | 4120952 |
| 3 | ISF003 | EVAPORATOR INSPECTION COMPARTMENT |  | 6C-187040018 (SX) |
|  |  |  |  | 6C-187040017 (DX) |
| 4 | ISF005 | EVAPORATOR HEAD | GALVANIZED SHEET SKIMPAS 7/10 | 6C-187040025 (SX) |
|  |  |  |  | 6C-187040024 (DX) |
| 5 | ISC013 | STAINLESS STEEL RESISTOR |  | 4120152 | 4120153 |
| 6 | ISF004 | DRAIN VALVE INSPECTION COMPARTMENT | GALVANIZED SHEET SKIMPAS 7/10 | 6C-187040020 (SX) |
|  |  |  |  | 6C-187040019 (DX) |
| 7 |  | VALVE THERMOSTAT.R404 TES 2 CART. |  | 4251313 |
| 8 | ISF014 | EQUALIZATION TUBE 2500 |  | 2C-250180004 | 2C-375180004 |
| 9 |  | VALVE BULB |  |  |
| 10 | ISF013 | DELIVERY TUBE |  | 2C-250180003 | 2C-375180003 |
| 11 |  | SUCTION TUBE |  | 2C-250180002 | 2C-375180002 |
| 12 | ISF006 P110-1 | EVAPORATOR CAPRI – SICILIA |  | 4220139 | 4220140 |
| 13 |  | SECURITY THERMOSTAT TYPE 2570 L |  | 4130114 |
| 14 | ISC016 | KLIXON SUPPORT | SILVER-PLATED + PLAST. ALUMINIUM 20/10 | 6C-187040039 |

3.4.2 FANS HOLDER

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | ISF002 | FANS HOLDER | GALVANIZED SHEET SKIMPAS 7/10 | 6C-250040023 | 6C-375040023 |
| 2 |  | MOTORFAN "PP" 4715 MS23TB10 A00 |  | 4241007 |

3.5 FRAME

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | ISB013 | FRONT FRAME RISER MILANO PAINTED |  | 2C-187002013 |
| 2 | I SB014 | FRAME WEIR | GALVANIZED SHEET 20/10 | 6C-187002014 |
| 3 | MIQ002_REV002 | FRAME ASSEMBLY MI PAINTED | IRON SHEET 25/10 | 2M-187001011 |

3.6 SLIDE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | NUT M18 |  |  |  |
| 2 | MIB004 | BRACKET FOR HANDLING SLIDE |  | 4282858 |
| 3 |  | GALVANIZED SCREW TTQST M.16X80 |  | 4331412 |
| 4 | MIB002_REV1 | HANDLING SLIDE MILANO | WOOD | 4321443 | 4321444 |

3.7 DRAIN

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | ALPHA" CURVE D40 2431 FINISH |  | 4102164 |
| 2 |  | HTB D.40 - 45° ELBOW "ALPHA" 802 |  | 4102168 |
| 3 |  | HTB D.40 - 87° ELBOW |  | 4102157 |
| 4 | ISI001 | RIGHT DRAIN SOCKET PIPE |  |  |  |
| 5 |  | TEE FINISH "ALPHA" 40 2403 SMOOTHED |  | 4102166 |
| 6 | ISI001 | LEFT DRAIN SOCKET PIPE |  |  |  |

3.8 CONTROL BOARD

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | ISC003 | ELECTRICAL COMPONENTS BOARD |  |  |
| 2 | ISC002 | RIGHT ELECTRICAL COMPONENTS BOARD SUPPORT BRACKET |  | 6C-187020005 |
| 3 | ISC004 | CLOSURE FOR ELECTRICAL COMPONENTS BOARD |  | 6C-187020007 |
| 4 | ISC002 | LEFT ELECTRICAL COMPONENTS BOARD SUPPORT BRACKET |  | 6C-187020006 |

3.9 FRONT GLASS

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 | ISD005 | CHAMBER GLASS RAIL-HAND PROFILE | GLASS CHAMBER RAIL-HAND PROFILE SILVER-PLATED ISM021-CP | 2C-250040035 | 2C-375040035 |
| 2 | ISD003 | GLASS 2 CHAMBER HARDENED 371,6X37,4 CAPRI |  | 4190264 | 4190265 |
| 3 | ISD004-CP | VERTICAL PVC CHAMBER GLASS PROFILE |  | 2C-187040034 (SX) |
|  |  |  |  | 2C-187040033 (DX) |
| 4 | ISD001 | LATERAL CLOSURE GLASS CHAMBER SUPPORT |  | 6C-187040032 |
| 5 | ISJ006 | FRONT TROLLEY STOPPER PROFILE | PVC TROLLEY STOPPER PROFILE SM VE. NEW L. 4500 1E-021 | 2C-250070007 | 2C-375070007 |
| 6 | ISD002 | FRONT GLASS SUPPORT PROFILE | GLASS CHAMBER SUPPORT PROFILE SP. SILVER-PALTED ISM017-CP | 2C-250070006 | 2C-375070006 |

3.10 CONTROL PANEL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2500 H225 P110 F350 | 3750 H225 P110 F350 |
| 1 |  | GEWISS L CABLE STOP |  |  |
| 2 | ISC001 | ELIWEL ELECTRONIC CONTROL SUPPORT | IRON SHEET 8/10 |  |

===========================================

Regione Gabannone, 4 – Zona Industriale

15030 TERRUGGIA (AL) ITALY

Tel.     +39 0142 433711

Fax.    +39 0142 433700