EXPLODED VIEW

VS-PORTOFINO

STATIC COOLING

GENERAL SPLITTING UP

- GLASSES SUPERSTRUCTURE

- INTERNAL FINISH, DISPLAY AREA

- FRONTAL DECORATION, FRAME, DRAIN

- CONTROL BOARD

- COMPLETE SIDE WALL

  - GLASSES SUPERSTRUCTURE

  - GLASS AND PROFILES

1.2  ALUMINIUM TOP AND LAMPS

1.3  GLASS UPRIGHT

1.4  BUMPER BAND

1.1  GLASS AND PROFILES

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | EEAV 106 | SILKSCREEN R1000 GLASS | FLOAT 6mm SILKSCREEN | 4191915 | 4191917 | 4191915 | 4191916 | 4191917 |
| 2 |  | GLASS GASKET PROFILE | PVC | 4180100 |
| 3 | DA0D 023 | JAW INSERT PROFILE CUT | ALUMINIUM PROFILE E5628A | 2PV120030006 | 2PV200030006 | 2PV120030006 | 2PV300030006 | 2PV200030006 |
| 4 | DA0D 015 | GLASSES JAW CUT AND DRILLING | ALUMINIUM | 2PV120030005 | 2PV200030005 | 2PV120030005 | 2PV300030005 | 2PV200030005 |

  - ALUMINIUM TOP AND LAMPS

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA0D 010 | LINEAR MODULE TOP PROFILE MOD 2380 | ALU. PROFILE Q 1238 | 2PV120030007 | 2PV200030007 | 2PV250030007 | 2PV300030007 | 2PV360030007 |
| 2 | ET0E 001 | TOP LAMP-HOLDER MOD 250 | PLAST SHEET 8/10 | 6BV120022004 | 6BV200022004 | 6BV250022004 | 6BV300022004 | 6BV360022004 |
| 3 |  | STARTER OSAMA ST 111 |  | 4116001 |
| 4 |  | LAMP-HOLDER + STARTER-HOLDER 249 TCR "UL | PVC | 4114726 |
| 5 |  | NEON CAP | PVC | 4114716 | 4114718 | 4114716 | 4114717 | 4114718 |
| 6 |  | NEON AKO PROTECTION TUBE | PVC | 4114716 | 4114718 | 4114716 | 4114717 | 4114718 |
| 7 |  | NEON |  | 30 Watt 4114510 | 58 Watt 4114511 | 30 Watt 4114510 | 36 Watt 4114512 | 58 Watt 4114511 |
| 8 |  | LAMP-HOLDER 249 TS "UL" | PVC | 4114727 |

1.3 CENTRAL UPRIGHT

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA0D 006 | FRONT UPRIGHT | ALUMINIUM ALLOY 6060 T5 | 4351214 |
| 2 |  | FRONT UPRIGHT SUPPORT | DRAWN IRON 4X40 | 2PV120030009 |
| 3 | DA0D 014 | RINFORCEMENT FOR FRONT UPRIGHT | GALVANIZED SHEET 15/10 | 6PV120030002 |
| 4 | RG 072 | UPRIGHT BACK PIN | RUNG STEEL Ø15 | 4140070 |
| 5 |  | WHITE CAP DP500 |  | 4333114 |
| 6 | TT0D 013 | UPRIGHT PIN | RUNG STEEL Ø15 | 4140088 |
| 7 | EEAV 011 | RIGHT ROTATION LEVER | ALUMINIUM ALLOY | 4282113 |
| 8 | ECAV 016 | PISTON NYLON BUSH | NYLON | 8291718 |
| 9 |  | SEGGER 5 | GALVANIZED STEEL | 8298303 |
| 10 | TT0D 024 | LEFT TOP FIXING BRACKET | IRON SHEET 15/10 | 2FI125030202 |
| 11 | TT0D 006 | CENTRAL BACKSIDE PIN | STEEL |  |  | 4140087 |
| 12 |  | PISTON STROKE 60 | STEEL | 4145020 | 4145023 | 4145020 | 4145021 | 4145023 |
| 13 |  | SPACER WITH HOLE DCK86 | NYLON | 8291721 |
| 14 | TT0D 001 | LEVER SUPPORT | IRON SHEET 20/10 | 2FI125030013 |
| 15 |  | SEGGER 7 | GALVANIZED STEEL | 8298304 |
| 16 | TT0D 024 | RIGHT TOP FIXING BRACKET | IRON SHEET 15/10 | 2FI125030201 |
| 17 | TT0D 004 | CENTRAL FRONTSIDE PIN | STEEL |  |  | 4140084 |
| 18 |  | PISTON FRONT PIN | STEEL | 4140054 |
| 19 | EEAV 011 | LEFT ROTATION LEVER | ALUMINIUM ALLOY | 4282114 |

1.3  RIGHT SIDE UPRIGHT

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA0D 006 | FRONT UPRIGHT | ALUMINIUM ALLOY 6060 T5 | 4351214 |
| 2 | DA0D 005 | FRONT UPRIGHT SUPPORT | DRAWN IRON 4X40 | 2PV120030009 |
| 3 | DA0D 014 | RINFORCEMENT FOR FRONT UPRIGHT | GALVANIZED DRAWN 15/10 | 6PV120030002 |
| 4 | RG 072 | FRONT UPRIGHT PIN | RUNG STEEL Ø15 | 4140070 |
| 5 |  | WHITE CAP DP500 |  | 4333114 |
| 6 | ECAV 018 | PISTON FRONT PIN | STEEL | 4140054 |
| 7 | EEAV 011 | RIGHT ROTATION LEVER | ALUMINIUM ALLOY | 4282113 |
| 8 | ECAV 016 | PISTON NYLON BUSH | NYLON | 8291718 |
| 9 |  | PISTON STROKE 60 | STEEL | 4145020 | 4145023 | 4145020 | 4145021 | 4145023 |
| 10 |  | SEGGER 7 | GALVANIZED STEEL | 8298304 |
| 11 |  | SPACER WITH HOLE DCS79B NYLON 6R ELECTROZUB | NYLON | 150 |
| 12 | TT0D 001 | LEVER SUPPORT | IRON SHEET 20/10 | 2FI125030013 |
| 13 | TT0D 024 | RIGHT TOP FIXING BRACKET | IRON SHEET 15/10 | 2FI125030201 |
| 14 | TT0D 015 | BACKSIDE PIN | DRAWN GROUND STEEL D 6 | 4140086 |
| 15 | TT0D 003 | FRONTSIDE PIN | DRAWN GROUND STEEL D 6 | 4140085 |
| 16 |  | SEGGER 5 | GALVANIZED STEEL | 8298303 |
| 17 | TT0D 013 | UPRIGHT PIN | RUNG STEEL Ø15 | 4140088 |

1.4 BUMPER BAND

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA0L 010 | GLASS LEDGE PROFILE (LINEAR MODULES) | ALUMINIUM | 2PV1200F0005 | 2PV2000F0005 | 2PV2500F0005 | 2PV3000F0005 | 2PV3600F0005 |
| 2 | DA0L 003 | CUT TROLLEY STOPPER MOD. 2380 | PVC | 2PV1200F0001 | 2PV2000F0001 | 2PV2500F0001 | 2PV3000F0001 | 2PV3600F0001 |
| 3 |  | BLACK GUM LEDGE GLASS PROFILE P0391 | 4180403 |

  - INTERNAL FINISH

2.1 DISPLAY PLATE

2.2 WORKING TABLE

2.3 UNDERSTORAGE DOOR

2.4 EVAPORATOR

2.5 INTERNAL FINISH

2.1 DISPLAY PLATE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | ET0K 010 | PLATE FOR STATIC COOLING | STAINLESS STEEL AISI304 8/10 | 6DS1200A2301 |

2.2 WORKING TABLE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA5H 004 | WORKING TABLE FOR STATIC COOLING | STAINLESS STEEL AISI304 8/10 | 2PS120010000 | 2PS360010000 | 2PS250010000 | 2PS300010000 | 2PS360010000 |
| 2 | ET0G 040 | THERMOMETER-HOLDER | STAINLESS STEEL AISI 304 10/10 |  |
| 3 |  | LCD THERMOMETER |  | 4131307 |

2.3 UNDERSTORAGE DOOR

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | EEE0 100 | DOOR | PST | 4331806 |
| 2 |  | HINGE 1 | PVC | 4330902 |

2.4 EVAPORATOR

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | ET0F 012 | EVAPORATOR FOR STATIC COOLING MOD. 250 | COOPER TUBES - ALUMINIUM SHEET | 4221700 | 4222110 (ETOF 011) | 4221702 | 4221703 | 4221704 |
| 2 |  | EVAPORATOR LIQUID SEPARATOR | COOPER TUBES |  |  |  |  |  |

2.4.1. EVAPORATOR WITH VALVE AND CAPILLARY TUBES

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 |  | CAPILLARY TUBE D. 1,4 X 2,60 | CAPILLARY | 4260203 | 4260203 | 4260204 | 4260204 | 4260204 |
| 2 |  | VALVE |  |  |  |  |  |  |
| 3 |  | SUCTION TUBE |  |  |  |  |  |  |
| 4 |  | PIPE UNION 1/2 SAE Ø12 |  |  |  |  |  |  |
| 5 |  | ANTICONDENSATE TUBE 6 X 15 | COOPER TUBES | 4270503 | 4270502 | 4270503 | 4270503 | 4270503 |
| 6 |  | EVAPORATOR-VALVE TUBE | COOPER TUBES |  |  |  |  |  |

2.5 INTERNAL FINISH

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA5G 001 | SUCTION GRID CLOSURE | STAINLESS STEEL AISI304 6/10 | 6PS120040004 | 6PS200040004 | 6PS250040004 | 6PS300040004 | 6PS360040004 |
| 2 |  | DRAIN D32 | ABS | 4102125 |
| 3 |  | DRAIN NUT D32 | ABS | 4102125 |
| 4 | ET0G 029 | LEFT STATIC BACK BRACKET | IRON SHEET 15/10 | 6BS120042001 (R) | 6BS120042002 (L) |
| 5 | ET0G 030 | RIGHT STATIC BACK BRACKET | IRON SHEET 15/10 |  | 6BS200042005 (R) | 6BS200042006 (L) |
| 6 | ET0G 031 | LATERAL INTERNAL UPRIGHT | ANODIZED ALUMINIUM PROFILE | 2BS120040003 |
| 7 | ET0U 001 | MULTIPLEXING BRACKET | STAINLESS STEEL AISI304 30/10 | 4282119 |
| 8 | EEAZ 129 | DRIP | STAINLESS STEEL AISI304 6/10 | 6BS120040001 | 6BS360040001 | 6BS250040001 | 6BS300040001 | 6BS360040001 |
| 9 | ET0G 033 | AIR OUTLET GRID STATIC | STAINLESS STEEL AISI304 8/10 |  |  |  |  |  |
| 10 | EEAZ 134 | BACK SUPPORT | ALUMINIUM PROFILE 25X25X3 |  |  |  |  |  |
| 11 | ET0G 034 | AIR OUTLET GRID STATIC | PLAST. SHEET 6/10 | 6DS120042003 | 6DS200042003 | 6DS250042003 | 6DS300042003 | 6DS360042003 |
| 12 | ET0G 031 | CENTRAL INTERNAL UPRIGHT | ANODIZED ALUMINIUM PROFILE | 2BS120040004 |
| 13 | ET0G 032 | FRONT PLATE SUPPORT STATIC | STAINLESS STEEL AISI304 6/10 | 6BS120042004 | 6BS300042004 | 6BS250042004 | 6BS300042004 | 6BS360042004 |
| 14 | ET0A 042 | LEFT BODY HEAD | STAINLESS STEEL AISI304 6/10 | 6BV120042016 |
| 15 | ET0A 042 | RIGHT BODY HEAD | STAINLESS STEEL AISI304 6/10 | 6BV120042015 |

3.  DECORATION – FRAME – DRAIN

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA0J 001 | UNDER-ENDWALL PANEL | PLAST. SHEET 6/10 | 6PV120080013 |
| 2 | ET0B 007 | LOADING SLIDE | SPRUCE WOOD | 4321219 | 4321223 | 4321221 | 4321222 | 4321223 |
| 3 | DA0J 002 | FRONTAL PANEL | LAM. PLAST. 6/10 | 2PV120070001 | 2PV300070001 | 2PV250070001 | 2PV300070001 | 2PV360070001 |
| 4 |  | BLACK ‘MINIGONNA’ PROFILE |  | 4161901 | 4161901 | 4161901 | 4161902 | 4161903 |
| 5 | DA0B 006 | LOADING SLIDE BLOCKING BRACKET | IRON SHEET 30/10 | 4282833 |
| 6 | ET0B 001 | FRAME | IRON 360 | 4280114 |
| 7 | ET0J 002 | SLOT PANEL FOR COMPRESSOR AREA | PLAST. SHEET 6/10 | 6BV120072009 | 6BV120072009 | 6BV120072009 | 6BV120072009 | 6BV120072009 |
| 8 | ET0J 003 | PIERCED BACK PANEL | PLAST. SHEET 6/10 | 6BV120072029 | 6BV200072029 | 6BV250072029 | 6BV300072029 | 6BV360072029 |
| 9 |  | DRAIN TUBE | PVC | 4180815 |

3.1.  LOADING SLIDE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | ET0B 007 | LOADING SLIDE LINEAR MOD. 250 | SPRUCE WOOD | 4321219 | 4321220 | 4321221 | 4321222 | 4321223 |
| 2 | ET0B 003 | SIDE MEMBER FOR COMPRESSOR AREA | IRON SHEET 15/10 | 6BV120002016 |
| 3 |  | FEET BOLT M12 | GALVANIZED STEEL | 8293413 |
| 4 | DA0B 006 | LOADING SLIDE BLOCKING BRACKET | IRON SHEET 30/10 | 4282833 |
| 5 |  | NUT M14 | GALVANIZED IRON |  |

3.2. DRAIN

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | ET0I 001 | DRAIN BASIN SUPPORT | SHEET 10/10 | 6BV120052001 | 6BV120052001 | 6BV120052001 | 6BV120052001 | 6BV120052001 |
| 2 |  | BASIN | PVC | 4100102 | 4100109 | 4100109 | 4100109 | 4100109 |
| 3 |  | PIPE D20 4102101 | ABS | 4102101 |
| 4 |  | PIPE NUT D20 | ABS | 4102101 |
| 5 |  | OREGON DRAIN TUBE | PVC | 4180815 |
| 6 |  | PIPE NUT D32 | ABS | 4102125 |
| 7 |  | PIPE D32 | ABS | 4102125 |

- CONTROL BOARD

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | MODULI/CODICI |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | ET0C 003 | ELECTRONIC FRONT CONTROL PANEL | PLAST. SHEET 6/10 | 6BV120020118 |
| 2 | ET0C 001 | BALLAST HOLDER | IRON SHEET 10/10 | 6BV120020182 |
| 3 |  | ELECTRONIC CONTROL ELIWELL |  | 4131712 |
| 4 |  | RELE FINDER 66.82.8.230.0300 |  | 4111012 |
| 5 |  | TRANSFORMER 12 V |  | 4131623 |
| 6 |  | END TERMINAL PA81 |  | 4113703 |
| 7 |  | BALLAST |  | 15 W 4115106 | 30 W 4115103 | 58 - 65 W 4115105 | 30 W 4115103 | 36 - 40 W 4115104 |
| 8 |  | FASTON TERMINAL PA 80 |  | 4113702 |
| 9 |  | BLACK BIPOLAR SWITCH |  | 4113518 |
| 10 | ET0C 004 | PVC CONTROL PANEL LABEL |  | 4335648 |
| 11 |  | PLUG |  |  |  |  |  |  |
| 12 |  | FEED CABLE |  |  |  |  |  |  |
| 13 | 8291719 | STOPPER FAIRLEAD HEYCO 6N3-4 | PVC | 8291719 |

5. COMPLETE SIDEWALL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1190 | 1785 | 2380 | 2975 | 3570 |
| 1 | DA0M 001 | END WALL | ABS | 4104027 |
| 2 |  | GLASS BLOCKING 1 | PVC | 4100313 |
| 3 | DA5M 001 | SIDE GLASS STATIC | FLOAT 6 mm | 4190327 |
| 4 | DA0J 001 | LEFT UNDER-ENDWALL SLOT PANEL | PLAST. SHEET 6/10 | 6PV120080003 |
| 5 | DA0M 007 | TOP SIDE HEAD | IRON SHEET 30/10 | 2PV120080002 |

===========================================

Regione Gabannone, 4 – Zona Industriale

15030 TERRUGGIA (AL) ITALY

Tel.     +39 0142 433711

Fax.    +39 0142 433700