EXPLODED VIEW

SYNUS

LOW TEMPERATURE

GENERAL SPLITTING UP

- INTERNAL FINISH, FRONTAL DECORATION

- GLASSES SUPERSTRUCTURE

- COMPLET SIDE WALL

- FRAME – LOADING SLIDE – BALLAST HOLDER PANEL

# 1. INTERNAL FINISH, FRONTAL DECORATION

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | SF0J008 | FRONT PANEL | GALVANIZED SHEET 7/10, PAINTED | 2IV125070001 | - |
|  | SF0J009 |  |  | - | 2IV250070002(DX) |
|  |  |  |  |  | 2IV250070003(SX) |
| 2. |  | FRONT FINISH |  |  |  |
| 3. |  | FIXED DIVIDER |  |  |  |
| 4. |  | EVAPORATOR |  | 2IV125141001 | 2IV250141001 |
| 5. |  | FANS HOLDER ASSEMBLY |  |  |  |
| 6. | SF6K007 | STAINLESS STEEL PLATE WITH HOLE BT 267 ASSEMBLY |  | 2IV125041127 |
| 7. | SF6K007 | STAINLESS STEEL PLATE WITHOUT HOLE BT 312 ASSEMBLY |  | 2IV125041124 |
| 8. |  | WORKING TABLE SYNUS BT |  | 2IV125011000 | 2IV250011000 |
| 9. |  | GLASS CHAMBER ASSEMBLY |  |  |  |
| 10. | SF6G014 | WHITE CENTRAL GLASS CHAMBER SUPPORT | POLYETHYLENE | - | 4081155 |
| 11. |  | BASIN INTERNAL FINISH |  |  |  |

1.1. BASIN INTERNAL FINISH

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | DRAIN D. 20 | ABS | 4102101 |
| 2. |  | DRAIN NUT D. 20 | ABS | 4102101 |
| 3. | SF6G007 | FRONT PLATE SUPPORT | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041011 | 6IV250041011 |
| 4. | SF6G001 | BACK AIR CHANNEL BRACKET | STAINLESS STEEL 304 2B 15/10 | 6IV125041112 (DX) |
|  |  |  |  | 6IV125041113 (SX) |
| 5. | SF6G002 | AIR OUTLET GRID MASK FOR FRONT UPRIGHT | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041009 | 6IV250041009 |
| 6. | SF6G004 | AIR OUTLET DIVERTER | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041010 | 6IV250041010 |
| 7. | SF6G009 | GLASS BAFFLE 1200 X 200 SY | FLOAT 6mm TRANSPARENT | 4190338 |
| 8. |  | DRAIN NUT D. 44 | ABS | 4102106 |
| 9. |  | LATERAL GLASS BLOCK | PVC | 4100313 |
| 10. | SF6G010 | GLASS CHAMBER CLOSURE - BASIN | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041140 |
| 11. |  | DRAIN 10124 1'1/2 GAS L.75 MM | ABS | 4102132 |
| 12. |  | DRAIN D. 44 | ABS | 4102106 |
| 13. |  | DRAIN NUT 1” 1/2 GAS | ABS | 4102132 |
| 14. | SFOL002 | GLASS REBATE PROFILE SUPPORT BRACKET | GALVANIZED SHEET 15/10 | 6IV1250F0001 (DX) |
|  |  |  |  | 6IV1250F0002 (SX) |
| 15 | SF6G006 | FRONT PLATE SUPPORT BRACKET | STAINLESS STEEL 304 2B 15/10 | 6IV125041114 (DX) |
|  |  |  |  | 6IV125041115 (SX) |

  - FIXED DIVIDER

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | CC6F010 | EVAPORATOR COVER SUPPORT | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6KV072041139 |
| 2. | SF6F003 | LATERAL EVAPORATOR CLOSURE | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6IV125041119 (DX) |
|  |  |  |  | 6IV125041120 (SX) |
| 3. | CC6F009 | FAN HOLDER SUPPORT | STAINLESS STEEL 304 1F/2B-2F/S4 5/10 | 6KV072041121 |
| 4. |  | FIXED DIVIDER ASSEMBLY |  | 2IV125041130 (DX) |
|  |  |  |  | 2IV125041136 (SX) |
| 5. |  | PROFILE |  |  |
| 6. | SF0U003 | LOW GLASS ON DIVIDER | FLOAT 6mm TRANSPARENT | 4190408 |
| 7. | SF6A008 | FRONT CLOSURE FOR WHITE FIXED DIVIDER | POLYETHYLENE |  |

  - FANS HOLDER

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | SF6F002 | FANS HOLDER | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6IV125041118 | 6IV250041118 |
| 2. | CC6F008 | VALVE INSPECTION | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6KV072041123 |
| 3. |  | MOTORFAN |  | 4241007 |
| 4. |  | CABLE CONNECTOR L. 1525 MM |  | 4110606 |
| 5. |  | SHUNT BOX D.65 GEWISS | PLAST INSULATING MAT. GW | 4115401 |

1.4. EVAPORATOR

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | CC6F001 | EVAPORATOR VL - BT | COOPER TUBES - ALUMINIUM SHEETS | 4390120 | 4390121 |
| 2. | SF6F001 | EVAPORATOR COVER | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6IV125041116 | 6IV250041116 |
| 3. |  | PIPE UNION 3/8SAE Ø8 |  | 4272415 |
| 4. |  | COOPER D. 10 X 12 (12 X 1) |  | 4260104 |
| 5. |  | WELDED VALVE THERMOSTAT.R404 TES/2 |  | 4251311 |
| 6. | PP441 | COOPER D.4X6 L.75 | COOPER TUBES D.4 X 6 | 4272414 |
| 7. | CC6F021 | LIQUID DISTRIBUTOR KREA | COOPER TUBES | 4272409 |
| 8. |  | CAPILLARY TUBE | COOPER TUBES 1.8X3 | 4260206 |
| 9. |  | VALVE BULB |  |  |
| 10. | SF6F012 | STAINLESS STEEL HEATER LT 300W/M |  | 4121923 | 4121924 |
| 11. |  | ANTICONDENSATE TUBE | INSULATING SPONGE 6 X 22 | 4270505 |
| 12. |  | SUCTION TUBE | COOPER TUBES 10X12 | 4260104 |
| 13. | CC6F019 | OUTLET COLLECTOR KREA | COOPER TUBES | 4272408 |

1.5. GLASS CHAMBER

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | SF6G013 | CHAMBER GLASS LATERAL GUIDE | POLYETHYLENE | 4081153 (DX) |
|  |  |  |  | 4081154 (SX) |
| 2. | SF6G015 | HEATER HOLDER FRAME | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041141 |
| 3. | SF6G018 | LOWER CHAMBER GLASS FLANGING | "U" RIGID PROFILE DA 20 IM08 | 2IV125041143 |
| 4. | SF6G012 | CHAMBER GLASS 3-6-3-6-3 1192X290 | FLOAT TRANSPARENT | 4190337 |
| 5. | CC0H014 | SILICONE HEATER 27W/MT |  | 4121006 |

1.6. WORKING TABLE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | SKIMMED LEVEL SURFACE FIRENZE |  | 2FI125010001 | 2FI250010001 |
| 2. |  | GREY GASKET ISOLENE ADHESIVE PE 160X5 |  | 4181801 |
| 3. | TT0H004 | BACK LEVEL SURFACE SUPPORT | IRON SHEET 20/10 | 6FI125010011(SX) |
|  |  |  |  | 6FI125010009(DX) |
| 4. | TT0H013 | BLIND WIREWAY | PLAST. SHEET 8/10 | 6FI125010007 | 6FI250010007 |
| 5. | TT0H014 | SLIDING GUIDE FOR ACCESSORIES | STAINLESS STEEL AISI304 8/10 | 6FI125010028 | 6FI250010028 |

  - FRONTAL FINISH

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | BLACK GLASS REBATE RUBBER PROFILE | RUBBER | 4180403 |
| 2. | SF0L 008 | FRONT PROFILE | ALLOY 6060 T5 | 2IV1250F0003 | 2IV2500F0003 |
| 3. | SF0G 012 | LATERAL UPRIGHT STOPPER | PLAST. SHEET 6/10 | 6IV1250F0007 (SX) |
|  |  |  |  | 6IV1250F0006 (DX) |
| 4. | SF0G 013 | CENTRAL UPRIGHT STOPPER | PLAST. SHEET 6/10 | 6IV1250F0005 | 6IV2500F0009(SX) |
|  |  |  |  |  | 6IV2500F0008(DX) |
| 5. | TT0G013 | UPPER BAFFLE PROFILE | PVC | 2FI125040007 | 2FI250040007 |
| 6. | SF6G017 | CHAMBER GLASS FRONT CLOSURE | STAINLESS STEEL 304 SB+PRO, 6/10 | 6IV125041142 |

  - PLATE WITH HOLE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | FAIRLEAD RUBBER D25 EZDG21 |  | 4113102 |
| 2. | SF6K002 | STAINLESS STEEL PLATE LT 267 WITH HOLE | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041128 |
| 3. | SF6K006 | INSULATED PLATE LT 267 |  | 4080715 |
| 4. | SF6K004 | UNDERPLATE LT 267 | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6IV125041129 |

  - PLATE WITHOUT HOLE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | SF6K001 | STAINLESS STEEL PLATE LT 312 WITHOUT HOLE | STAINLESS STEEL 304 SB+PRO 8/10 | 6IV125041125 |
| 2. | SF6K005 | INSULATED PLATE LT 312 |  | 4080714 |
| 3. | SF6K003 | UNDERPLATE LT 312 | STAINLESS STEEL 304 1F/2B-2F/S4 6/10 | 6IV125041126 |

# 2. GLASSES SUPERSTRUCTURE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | GLASS FIXING PLIERS |  | 2FI125030006 | 2FI250030006 |
| 2. |  | LATERAL UPRIGHT |  |  |
| 3. | SF0M003 | GLASS SIDE HEAD | RIM / PUR D. 350 Kg/m³ | 2IV125080013 (SX) |
|  |  |  |  | 2IV125080003 (DX) |
| 4. |  | UPPER CEILING LAMP |  | 2FI125030009 | 2FI250030009 |
| 5. | SF0D021 | LEVER CLOSURE TUBE | ALUMINIUM TUBE Ø28 Th. 1.5 | 2IV125030006 | 2IV250030006 |
| 6. | SF0D002 | HEAD GLASS | FLOAT 10mm | 4199915 | 4199915 |
| 7. |  | CENTRAL UPRIGHT |  |  |

2.1. LATERAL AND CENTRAL GLASS UPRIGHT

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 | 3750 |
| 1. | TT0D002 | CURVED FRONT UPRIGHT | ALLOY 6060 T5 | 4351209 |
| 2. |  | WHITE STOPPER DP500 | PLASTIC | 4333114 |
| 3. |  | CAGE NUT M5 |  |  |
| 4. |  | SPACER WITH HOLE 1D-003 | NYLON | 4331409 |
| 5. | ECAV 016 | PISTON BUSH | NYLON | 8291718 |
| 6. |  | SEGGER 5 | GALVANIZED STEEL | 8298303 |
| 7. | TT 0D001 | LEVER SUPPORT | IRON SHEET 20/10 | 2FI125030013 |
| 8. |  | PLAIN RING 8X24 | GALVANIZED STEEL |  |
| 9. |  | GROWER M8 |  |  |
| 10. | RG072 | BACK GLASS UPRIGHT PIN | STEEL BAR Ø15 | 4140070 |
| 11. |  | BOLT TCEI M8X30 | GALVANIZED STEEL |  |
| 12. |  | BOLT TS+ M5X35 | STAINLESS STEEL |  |
| 13. | SF0D017 | LATERAL LEVER COVER | GALVANIZED SHEET 15/10 | 2IV125030004 (SX) |
|  |  |  |  | 2IV125030003 (DX) |
| 14. |  | RUBBER BUFFER |  | 4332602 |
| 15. |  | SPACER WITH HOLE DCS79B 6R ELECTROZUB | NYLON |  |
| 16. | TT0D005 | LATERAL BACK PIN | GROUND DRAWN STEEL Ø8 | 4140086 |
| 17. |  | SEGGER 7 | GALVANIZED STEEL | 8298304 |
| 18. |  | PISTON VS-SV R 1000 084034 700 N | STAINLESS STEEL | 4145022 |
| 19. | ECAV018 | PISTON FRONT PIN | GROUND DRAWN STEEL Ø6 |  |
| 20. | TT0D003 | LATERAL FRONT PIN | GROUND DRAWN STEEL Ø6 | 4140085 |
| 21. | AV011 | ROTATION LEVER PRESSOFUS | ALUMINIUM ALLOY | 4282114 (SX) |
|  |  |  |  | 4282113 (DX) |
| 22. | TT0D013 | GLASS UPRIGHT PIN | STEEL BAR Ø15 | 4140088 |
| 23. | TT0D006 | CENTRAL BACK PIN | GROUND DRAWN STEEL Ø8 | 4140087 |
| 24. | TT0D004 | CENTRAL FRONT PIN | GROUND DRAWN STEEL Ø6 | 4140084 |
| 25. | SF0D018 | CENTRAL LEVER COVER | GALVANIZED SHEET 15/10 | 2IV187030005 |

2.3. CEILING LAMP

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | TT0E002 | CEILING LAMP PROFILE | ANODIZED ALUMINIUM | 2FI125030010 | 2FI250030010 |
| 2. | TT0E014 | TOP LAMPS HOLDER | PLASTICIZED SHEET 8/10 | 6FI125030011 | 6FI125030011 |
| 3. | CC0D023.1 | PLEXIGLAS FOR CEILING LAMP | OPAL GLASS 3mm | 4082305 |
| 4. |  | LAMPS HOLDER + STARTERS HOLDER STUCCHI 255/C | PVC | 4114710 |
| 5. |  | NEON 30 W/76 D.26 L 900 |  | 4114510 |
| 6. | TT0E015 | TOP POLYCARBONATE CEILING LAMP | POLYCARBONATE 7/10 | 6FI125030012 | 6FI125030012 |
| 7. |  | UNIVERSAL STARTER FS 11 |  | 4116001 |
| 8. |  | LAMP HOLDER STUCCHI 255/S 2A 250V | PVC | 4114709 |

2.4. FRONT GLASS

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | TT0D011 | JAW PROFILE | JAW ALUMINIUM PROFILE | 2FI125030007 | 2FI125030007 |
| 2. | TT0D031 | JAW INSERT PROFILE | ALUMINIUM PROFILE | 2FI125030008 | 2FI125030008 |
| 3. |  | GLASS GASKET PROFILE | PVC | 4180100 |
| 4. | RG004.1 | CURVED GLASS | FLOAT 6 mm | 4190739 | 4190739 |

- COMPLETE SIDE WALL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 |
| 1. | SF0M001 | SIDE WALL SYNUS POL. PAINTED | POLYURETHANE Th. 50mm | 2IV125080012 (SX) |
|  |  |  |  | 2IV125080002 (DX) |

- FRAME – LOADING SLIDE – BALLAST HOLDER PANEL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | LATERAL FRAME ASSEMBLY |  |  |  |
| 2. |  | CENTRAL FRAME ASSEMBLY |  |  |  |
| 3. |  | BALLAST HOLDER PANEL |  |  |  |
| 4. |  | LOADING SLIDE |  |  |  |
| 5. | SF0L003 | TROLLEY STOPPER TUBE | TUBE PROFILE STAINLESS STEEL 22X1,5 L.6000 | 2IV1250F0004 | 2IV2500F0004 |

4.1. LATERAL FRAME ASSEMBLY

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | SF0B 003 | CASE CLOSURE | ABS | 4100339 (SX) |
|  |  |  |  | 4100338 (DX) |
| 2. | SF0B 001 | FRAME | ALUMINIUM ALLOY | 2IV125060001 |
| 3. | SF0B 005 | SPRING FOR LATERAL CLOSURE COUPLIG | STAINLESS STEEL AISI301 5/10 | 4282798 |
| 4. | SF0B 004 | LATERAL FRAME CLOSURE | GALVANIZED SHEET 10/10 | 2IV125080014 (SX) |
|  |  |  |  | 2IV125080004 (DX) |
| 5. |  | NUT SPACER M14 | GALVANIZED IRON |  |
| 6. | SF0B 008 | LOADING SLIDE FIXING BRACKET | IRON SHEET 30/10 | 4282832 |
| 7. |  | BOLT M12X45 | GALVANIZED STEEL |  |
| 8. | SF0J 007 | FRONT SIDE WALL STOPPER | GALVANIZED SHEET 7/10 | 2IV125070005 (SX) |
|  |  |  |  | 2IV125070004 (DX) |
| 9. | SF0B 010 | CASE FIXING BRACKET | GALVANIZED SHEET 10/10 | 6IV125060003 (SX) |
|  |  |  |  | 6IV125060002 (DX) |

4.2. CENTRAL FRAME ASSEMBLY

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | SF0B 001 | FRAME | ALUMINIUM ALLOY | - | 2IV125060001 |
| 2. |  | NUT SPACER M14 | GALVANIZED IRON | - |  |
| 3. | SF0B 008 | LOADING SLIDE FIXING BRACKET | IRON SHEET 30/10 | - | 4282832 |
| 4. |  | BOLT M12X45 | GALVANIZED STEEL | - |  |

4.3. LOADING SLIDE

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. | TT0B 014 | LOADING SLIDE | SPRUCE WOOD | 4321345 |
| 2. |  | SPLINE | WOOD 80 X 50 X 630 | 4321248 |

4.4. BALLAST HOLDER PANEL

| ITEM NUMBER | DOCUMENT NUMBER | TITLE | MATERIAL | PART NO. FOR EACH MODULE |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1250 | 2500 |
| 1. |  | BALLAST PANEL | IRON SHEET 10/10 | 2IV125090003 |
| 2. |  | BALLAST |  | 15W | 18 – 20 W | 30W | 36 – 40 W | 58 – 65 W |
|  |  |  |  | 4115106 | 4115102 | 4115103 | 4115104 | 4115105 |

===========================================

Regione Gabannone, 4 – Zona Industriale

15030 TERRUGGIA (AL) ITALY

Tel.     +39 0142 433711

Fax.    +39 0142 433700